## Slide 1: Pool Chemical Calc
Minimum Viable Product Requirements

## Slide 2: Customer Details
Name:
Address:
Mobile:
Email:
Pool Size: in Litre
Sanitiser: (Options to select)
  Salt
  Liquid Chlorine
  Stabilised Di-Chlor / 3 in 1
  Cal-Hypo

## Slide 3: Calculator Logic (Please ignore)
Parameter | Target Range | Logic
Total Alkalinity | 80-120ppm | To be filled – Jing’s Action
pH | 7.2-7.6 | To be filled – Jing’s Action
Free Chlorine | 2-4ppm | To be filled – Jing’s Action
Total Hardness | 150-250ppm | To be filled – Jing’s Action
Stabiliser | 40-100ppm | To be filled – Jing’s Action
Phosphate | <0.2ppm | To be filled – Jing’s Action
Salt | 3500-4500ppm | If (Test Value < Target Range) Add Salt = [(Target Range – Test Value) / 1000 * Pool Size in litre /1000] KG else Remove and refill some water in Litre

## Slide 4: TA – Calculator Logic
Parameter | Target Range
Total Alkalinity | 80-120ppm
If too low | Add pH Buffer (KG) = (100ppm – current value) / 10ppm * 0.2 * (pool size in litre / 10000 litre)
If too high* | Seek Professional Advice (Reduce pH to 7.0-7.2 with acid, then add pH up to raise pH)

## Slide 5: pH (too high) – Calculator Logic
Parameter | Target Range
pH | 7.2-7.6
If too high | Add Pool Acid result (ml)
Calculator Logic | 
delta = 7.4 – current value; delta = delta * (Pool Size in Litre / 3.78541); temp = (current value + 7.4) / 2; adj = (192.1626 + -60.1221 * temp + 6.0752 * temp * temp + -0.1943 * temp * temp * temp) * (TA current value + 13.91) / 114.6; delta = delta * adj; result = (delta / -240.15) ; result = result * 0.0283595 + 0.5 ; | 

## Slide 6: pH (too low) – Calculator Logic
Parameter | Target Range
pH | 7.2-7.6
If too low | Add pH up (g)
Calculator Logic | 
delta = 7.4 – current value; delta = delta * (Pool Size in Litre / 3.78541); temp = (current value + 7.4) / 2; adj = (192.1626 + -60.1221 * temp + 6.0752 * temp * temp + -0.1943 * temp * temp * temp) * (TA current value + 13.91) / 114.6; delta = delta * adj; result = delta / 218.68 result = result * 28.3495 + 0.5 | 

## Slide 7: FC – Calculator Logic
Parameter | Target Range
Free Chlorine | 2-4ppm
If too low | Add If Liquid Chlorine (ml) = (3ppm – current value) * (Pool Size in Litre / 3.78541 ) / 482.202 * 6 / 12.5 x 29.5735 + 0.5 If Stabilised Di-Chlor / 3 in 1 (g) = (3ppm – current value) * (Pool Size in Litre / 3.78541 ) / 4149.03 * 28.3495 + 0.5 If Cal-Hypo (g) = (3ppm – current value) * (pool size / 3.78541) / 5199.52 * 28.3495 + 0.5 If Salt Chlorinator, crank up production
If too high | Add Chlorine Remover (g) = (current value – 3ppm) * Pool Size in Litre / 10000 Litre * 10g

## Slide 8: CH – Calculator Logic
Parameter | Target Range
Total Hardness | 150 – 250 ppm
If too low | Add Calcium Hardness (KG) = (200ppm – current value) / 10ppm * 0.1 * (Pool Size in Litre / 10000 Litre)
If too high | Remove (100 – 200ppm / current value * 100) % of water and refill with clean fresh water

## Slide 9: CYA/Stabiliser – Calculator Logic
Parameter | Target Range
Stabiliser | 30-100ppm
If too low | Add Stabiliser (KG) = (40ppm – current value) / 20ppm * 0.2 * (Pool Size in Litre / 10000 Litre)
If too high | Remove (100 – 40ppm / current value * 100) % of water and refill with clean fresh water

## Slide 10: Phosphate – Calculator Logic
Parameter | Target Range
Phosphate | < 0.2ppm
If between 0.2 to 2.0ppm | Add Phosphate Remover (ml) = Pool Size in Litre / 10000 Litre * 100 ml * current value
If above 2.0ppm | Add Phosphate Remover (ml) = Pool Size in Litre / 10000 Litre * 200 ml * current value

## Slide 11: Salt – Calculator Logic
Parameter | Target Range
Salt | 3500 – 4500 ppm
If too low | Add Salt (KG) = (4000ppm – current value) / 1000 * Pool Size in Litre / 1000
If too high | Remove (100 – 4000ppm / current value * 100) % of water and refill with clean fresh water

## Slide 12
Product Type or action | Product Type Alias | Chemistry | Drection
Pool Acid |  | pH | too high
 |  | pH | too low
 |  | CALCIUM HARDNESS | too high
 |  | CALCIUM HARDNESS | too low
 |  | FREE_CHLORINE | too high
 |  | FREE_CHLORINE | too low
 |  | TOTAL_ALKAINITY | too high
 |  | TOTAL_ALKAINITY | too low
 |  | STABILISER | too high
 |  | STABILISER | too low
 |  | SALT | too high
 |  | SALT | too low
 |  | Total Chlorine | too high
 |  | Total Chlorine | too low